## Slide 1
Adaptive Robustness Margins for CBFs
via Privileged-Observation Reinforcement Learning — A Quadrupedal Safety-Filter Case Study
Xianmai Liang

## Slide 2
The problem with safe robots
CBFs in theory. Reduce safety to a pointwise affine constraint on the control input — solve a small QP, get formal forward-invariance of the safe set.
Reality breaks every assumption. Friction varies, payloads shift the COM, perception is noisy, the robot has a body.
Robust CBF variants add tightening parameters (α, φ, a, c) — but worst-case-derived values are crushingly conservative. The robot freezes or refuses to move.
Hand-tuning is the practical workaround. But it's brittle to environments unlike the tuning set, and gives no recipe for new scenes.

## Slide 3
Research question
Can a learned policy adapt the robust-CBF parameters online,
conditioning on what the environment currently looks like?
Approach: borrow the Rapid Motor Adaptation (RMA) architecture — a privileged-observation teacher reads dynamics + a top-down occupancy grid, and outputs the robustification tuple (α, φ, a, c) per timestep, feeding a robust-CBF QP that wraps an off-the-shelf locomotion controller.
Non-negativity is enforced by construction → qualitative robust-safety guarantee preserved for whatever uncertainty bounds the policy chooses.

## Slide 4
Background: control barrier functions
Safe set C = { x : h(x) ≥ 0 }. A CBF condition tightens to a pointwise affine constraint on the control:
L_f h(x) + L_g h(x) · u ≥ −α · h(x)
Robust variants (Kolathaya 2018 ISSf, Cosner 2022 TISSf, Dean 2019, Molnar 2021) tighten the RHS:
L_g h · û − φ ‖L_g h‖² − a − b ‖û‖₂ + α (h − c) ≥ 0
Each tightening parameter absorbs a specific class of uncertainty. Set them too large → frozen robot. Set them too small → safety guarantee shrinks.

## Slide 5
The four-parameter action space
Each parameter maps to a specific uncertainty class — the policy adapts them per timestep.
Param | Range | Role | Uncertainty class
α | [0.1, 5.0] | Class-K slope on shifted h(x) − c | Model / tracking error
φ | [0.0, 5.0] | Coefficient on ‖L_g h‖² | Actuation uncertainty (ISSf)
a | [0.0, 0.5] | Additive RHS slack | Measurement uncertainty
c | [0.0, 0.5] | Inward shift of safe-set boundary | Boundary correction
b | (unused) | Reserved for input-dep slack b‖u‖ | Would require SOCP
Output non-negativity → robust-safety theorem (Cosner 2022) holds for whatever uncertainty bounds the policy's outputs encode.

## Slide 6
Method: privileged-obs teacher → robust-CBF QP
Privileged obs 8207-D
CNN+MLP encoder → Z(12)
π_teacher → (α, φ, a, c)
Robust-CBF QP (closed-form)
Locomotion (frozen)
Drop-in safety filter: the locomotion controller is fixed and frozen — works with any user's stack.
• Single-integrator surrogate: ẋ_robot = u → QP is a closed-form half-space projection on GPU (no infeasibilities observed).
• Robot footprint enters as Minkowski expansion by 0.15 m so h = 0 aligns with physical contact.
• u_des never enters the network — it is a sidecar to the CBF, only used in reward (‖u_safe − u_des‖²).
• Per-step adaptation distinguishes us from per-episode α-calibration baselines (e.g., SHIELD).

## Slide 7
Privileged observation + network architecture
Privileged observation (8207-D)
Block | Dim | Content
Dynamics | 15 | Body velocities, ext. force/torque, friction, COM offset, last action
Occupancy grid | 2 × 64 × 64 | Two-frame top-down, 0.1 m / cell, 6.4 m FOV
Two-frame stacking encodes obstacle motion (grid_t − grid_{t−1}).
Network (~600 k actor params)
• Grid: Conv(2→16, s=2) → Conv(16→32, s=2) → Linear(8192→64)
• Dynamics: Linear(15 → 64)
• Concat → Linear(128 → 128) → Linear(128 → z)
• Latent: Z ∈ ℝ¹² (RMA-style bottleneck; get_z(obs) exposed)
• π-head: Z → (α, φ, a, b, c), tanh-squash to physical range
• V-head: separate critic encoder (no shared params)

## Slide 8
Reward design + training
Reward stack (5 terms)
Term | Weight | Trigger
collision | −100 | obstacle contact (terminal)
infeasibility | −10 / step | QP infeasible
u_safe deviation | −0.1 ‖u_safe − u_des‖² | per-step (light-touch filter)
proximity | −1.0 · exp(−min_sdf / 0.5) | per-step (gradient near obstacles)
action_rate | −5×10⁻³ ‖Δa‖² | per-step (smooth CBF params)
Negative results we recorded
• Proximity = −5 → policy maxed distance instead of progress (φ̄ rose to 2.79). Halved to −1. • Weight decay 1e-4 → action_std collapsed to 0.06; exploration died. Final: 1e-5 + entropy 5e-3.
Training (PPO)
4096 parallel envs × 3000 iters (~3 h on RTX 5090)
AdamW, weight_decay = 1e-5
entropy_coef = 5e-3 (load-bearing)
Episode length 20 s
Domain randomization (per-reset)
• friction: μs ∈ [0.30, 1.20], μd ∈ [0.20, 1.00]
• external force ±10 N, torque ±2 Nm
• COM offset ±5 cm xy / ±3 cm z
Multi-planner mix (the deploy-realistic distribution)
• smooth_goal 0.40 / waypoint 0.25 / mpc 0.20
• walk 0.05 / adversarial 0.05 / legacy 0.05

## Slide 9
Evaluation: 24-config baseline sweep
Each baseline is a special case of the same robust-CBF constraint. We tune each family's grid and report the BEST configuration per task.
Family | Form | Grid | # configs
B0 (plain) | φ = a = c = 0; α only | α ∈ {0.5, 1.5, 3.0} | 3
B1 (ISSf) | φ scalar, a = c = 0 | α × φ ∈ {0.5, 1.5, 3.0}² | 9
B2 (TISSf) | φ(h) = (1/ε₀) exp(−λh), a = c = 0 | α × ε₀ × λ (3 × 2 × 2) | 12
RL-CBF (ours) | Per-step learned (α, φ, a, c) | — | 1
Metric: combined fall + stuck rate
Fall = body-contact-with-floor termination. Stuck = horizontal speed below 0.10 m/s for more than half the episode. Including stuck is critical: earlier evals hid a 22-pp block of failures inside "timeout successes" — a robot frozen safely is not a useful robot.

## Slide 10
Headline result (in-distribution)
RL-CBF achieves the lowest fall, lowest stuck, and lowest combined failure of any of the 25 configurations evaluated.
Mode | Best config | Fall | Stuck | Combined | h̄ | φ̄
B0 plain | α = 0.50 | 0.293 | 0.226 | 0.519 | 0.305 | 0.005
B1 ISSf | α = 0.50, φ = 1.50 | 0.296 | 0.119 | 0.415 | 0.371 | 1.50
B2 TISSf | α = 1.50, ε₀ = 0.50, λ = 1.0 (best B) | 0.243 | 0.132 | 0.375 | 0.371 | 1.43
RL-CBF (ours) | teacher policy | 0.231 | 0.075 | 0.306 | 0.413 | 0.91
+6.9 pp WIN on combined fall + stuck vs. the best of 24 hand-tuned baselines
Statistical caveat: ~134 episodes per config → SE ≈ 3–4 pp; the gap is ~2σ. Camera-ready run will use paired evaluation (variance ↓ 5–10×).

## Slide 11
Why does it win? Behavioral reading
Hand-tuned baselines that match RL-CBF's fall rate buy that safety with a bigger nominal margin (high φ̄).
RL-CBF: same fall safety + LOWER φ̄ (0.91) + HIGHER h̄ (0.413)
It lets the robot operate closer to its (relaxed) safety boundary while keeping larger absolute distance from obstacles.
The mechanism is adaptation:
→ Spend robustness budget where the scene calls for it.
→ Save it where it does not — open space, slow-moving obstacles, robot on solid ground.
→ Static baselines can't do this — they apply the same robustness everywhere.

## Slide 12
Out-of-distribution generalization (5 single-knob shifts)
Each shift pushes ONE randomization axis past the training range while keeping the others at training distribution.
Eval axis | Type | RL-CBF combined | Best baseline | Margin
In-dist (ref) | mixed | 0.306 | 0.375 | +6.9 pp
Slippery | priv-obs (continuous friction) | 0.411 | 0.453 | +4.1 pp
HighDisturbance | priv-obs (episodic force / torque) | 0.341 | 0.431 | +9.0 pp
HeavyCOM | priv-obs (startup COM bias) | 0.331 | 0.390 | +5.9 pp
FastObstacles | priv-obs (grid history) | 0.338 | 0.444 | +10.5 pp
DensePack | scene-only (h(x) symmetric) | 0.338 | 0.344 | +0.5 pp (tie)
RealisticCompound | all 5 simultaneously | 0.500 | 0.497 | −0.3 pp (tie)
5 priv-obs WINS (+4.1 to +10.5 pp) · 1 scene-only TIE · 1 compositional TIE

## Slide 13
The pattern is sharper than "wins everywhere"
RL-CBF wins on every axis whose disturbance signal is in the privileged-observation vector, and ties the best baseline within statistical noise on scene-only shifts.
Wins (priv-obs aligned)
✓ Slippery — friction in dyn block
✓ HighDisturbance — applied force in dyn block
✓ HeavyCOM — COM offset in dyn block
✓ FastObstacles — motion via grid history
✓ (In-dist headline: all of the above)
Ties (playing field is symmetric)
≈ DensePack — only h(x) shifts; baselines see the same h
≈ RealisticCompound — joint high-tail not in training distribution
→ The win comes specifically from privileged information — exactly as the architecture was designed to.

## Slide 14
Limitations + future work
Sim-only — sim-to-real transfer of a learned safety filter requires three things we have not done
(i) Calibrate the LiDAR-derived occupancy grid against real Mid-360 data — drop-out and spurious-return rates we did not inject during training.
(ii) Replace the analytical SDF with a distance-transformed occupancy grid at deploy time (close the train/deploy h-pipeline gap).
(iii) Student distillation step: (LiDAR + base_vel + history) → Ẑ ∈ ℝ¹² → frozen π_teacher. RMA student-side; standard recipe.
Other open items
• b slot reserved but unused → would require SOCP solver instead of closed-form half-space projection.
• Compositional generalization (RealisticCompound tie) → joint high-tail untrained.
• Paired evaluation (same seed list across all 25 configs) → variance reduction 5–10× for camera-ready.

## Slide 15
Summary
A privileged-observation RL teacher learns the four robust-CBF parameters per timestep. Beats the best of 24 hand-tuned baselines by +6.9 pp combined fall + stuck in-distribution. Wins on every privileged-obs aligned OOD axis. Ties on scene-only / compositional shifts.
Why this matters
→ Robust-CBF parameters can be adapted online — no need to commit to one conservative tuple.
→ Drop-in design: works with any frozen locomotion stack. Safety guarantee preserved by output non-negativity.
→ Per-step adaptation gives a clean differentiation from per-episode α-calibration baselines (e.g., SHIELD).
Questions?